## Slide 1: Wireless communication lab
Lab report
NAME: Qiusi Shen
ID: 004749315

## Slide 2: Abstraction
This two lab focus on wireless communication and analysis its behavior
The wireless LAN setup utilizes the Infrastructure-mode of the 802.11b. Wireless LAN adapters in conjunction with a Linksys access point.
One laptop will be stationary and other laptop will connect to that client. Use the DHCP dynamic host configuration protocol server provided by the access point, and the IP address will be dynamically allocated as done in home or public access wireless networks.
Iperf is a tool for measuring the TCP and UDP bandwidth performance. The tool was developed at the NLANR national laboratory for Applied Network

## Slide 3: Background
For UDP measurement, an Iperf client sends a constant bit rate stream to the Iperf server. Since it is pre-determined what the Iperf UDP client will send to the Iperf UDP server. The server is periodically report the number of datagram lost in the transmission.
For TCP measurement, an Iperf TCP client connects to the Iperf server and the server attempts to send as much data as it can for a fixed time. Then

## Slide 4: TCP and UDP Throughput vs Signal strength
Location | Distance | Signal Strength | Noise Power | SNR | UDP | TCP | Observatio-n
Wall 3704 entry | 30ft | -38 | -83 | 45 | 13500 | 13300 | 2datagrams received out of order
3428 main entry | 60ft | -48 | -82 | 34 | 14300 | 6100 | 1datagrams received out of order
3424 entry | 90ft | -50 | -87 | 37 | 7840 | 988 | 1datagrams received out of order

## Slide 5: Noise and Thought with Microwave Oven
Level | Signal Strength | Noise Power | UDP | TCP | Observation | Other
Off | -12 | -80 | 21200 | 5750 | Flat | 1 datagram out of order
High | -12 | -83 | 17100 | 2300 | Slight bump | 1 datagram out of order
Medium high | -14 | -80 | 6550 | 11700 | Slight bump | 1 datagram out of order
Medium | -8 | -80 | 5250 | 15300 | Slight bump | 1 datagram out of order
Defrost | -8 | -80 | 9080 | 60500 | Slight bump | 1 datagram out of order
Warm | -12 | -81 | 2450 | 14600 | flat | 1 datagram out of order

## Slide 6: Distance vs Signal Strength
Chart: 
| 0 | 1 | 2
 | 21200 | 24500 | 9080

## Slide 7: UDP Throughput vs signal to noise ratio
Chart: 
| 0 | 1 | 2
 | 21200 | 24500 | 9080

## Slide 8: TCP Throughput vs signal to noise ratio
Chart: 
| 0 | 1 | 2
 | 21200 | 24500 | 9080

## Slide 9: Throughput against microwave level
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5
 | 21200 | 24500 | 9080 | 5250 | 6550 | 17100
 | 5570 | 1460 | 6050 | 1530 | 1170 | 2300

## Slide 10: Result
Decreasing in the signal strength of any wireless LAN signal decreasing with the increasing in distance
The stronger signal it is, the faster the data throughput for either of the transmission protocols will be
More noise and interference from the microwave results in a significantly lower data throughput

## Slide 11: Lab data
Distance | Packet Type | Data Rate | Observation
10ft | DH1 | 190.284 | Every 7 outputs rate drop
 | DH3 | 208.114 | Every 6 outputs rate drop
 | DH5 | 264.081 | Every 6 outputs rate drop
15ft | DH1 | 127.451 | Took longer to start
 | DH3 | 197.452 | Every 6 outputs rate drop
 | DH5 | 165.422 | Every 3 outputs rate drop
30ft | DH1 | 120.184 | Every 3 outputs rate drop
 | DH3 | 59.508 | Every 3 outputs rate drop
 | DH5 | 85.583 | Every 3 outputs rate drop

## Slide 12: Data Throughput vs # of slaves
Number of Masters | Packet type | Data Rate
1 | DH1 | 55.2
 | DH3 | 83.7
 | DH5 | 275
2 | DH1 | 11.762
 | DH3 | 47.6
 | DH5 | 65.2
3 | DH1 | 7.30
 | DH3 | 30
 | DH5 | 38.4

## Slide 13
Measurement Case | Data Rate for each pair of connections
Before interference | 170
3 Connections crossing | 170-270
 | 85-270
 | 170-260
 | Data Rate
Bluetooth Throughput | 260
802.11b TCP Throughput | 8.05

## Slide 14: Data Throughput vs Distance DH1 DH3 Dh5
Chart: 
| 10 | 15 | 30
 | 190.284 | 127.451 | 120.184
 | 208.114 | 197.452 | 59.508
 | 264.081 | 165.422 | 85.583

## Slide 15: Result
As the distance from the master source increases the overall data throughput decreases
Data throughput values with Bluetooth are much lower than that of both UDP and TCP WLAN protocols
The wave is not clear enough in the lab so the result might not be that accurate

## Slide 16: Conclusion
The lab is focus on analysis different behavior of wireless communication. Also, compared the difference between UCP and TCP which is very important in study.
We also discovered the facts like decreasing in the signal strength of any wireless LAN signal decreasing with the increasing in distance from the data
We also conclude the DH1, DH3, DH5 has little difference behavior
Also , the wifi is a more reliable way for wireless communication than the bluetooth